Faraday - Anechoic Chamber法拉第-电波暗室

An anechoic chamber offers you a Superb Shielding Performance一个电波暗室提供你一个杰出的屏蔽性能

We has experience in all types of EMC anechoic chambers and designs.

我们有经验在所有类型的EMC电波暗室和设计。

Our Anechoic Chambers are constructed as shielded rooms. All over the walls and the ceiling, absorbing materials and/or ferrite tiles are attached. The Anechoic Chambers show superb shielding performance and are mainly applied in EM emission testing according to commercial and military standards.

我们的电波暗室被建造为屏蔽室。墙和顶棚各处，吸收材料和/或铁氧体瓦片被附加。电波暗室显示出杰出的屏蔽性能和主要应用在EM电磁发射测试依据商业和军用标准。

The Anechoic Chambers are used to perform compliant radiated immunity tests in accordance to EMC-standards such as IEC / EN 61000-4-3.

该电波暗室被用于执行符合性辐射抗扰度测试依照EMC标准，如：IEC/EN61000-4-3.

They provide a full compliance immunity test site for the frequency range of 26Mhz to 18GHz.

它们提供了一个全兼容的抗干扰测试场地用于频率范围 26Mhz - 18GHz

Also suitable for future free space emission test, pr EN 50147-3.

也适合于将来的自由空间辐射测试，pr EN 50147-3.

We can also build open area test sites.

我们也能建造开阔场地试验场地。

Emission Performance发射性能 – 26MHz-18GHz

Immunity抗干扰度 26 MHz-18GHz

Key features关键特点:

- Fully compliant design to meet UKAS and FCC requirements 全兼容设计以满足UKAS和FCC要求。

- All dimension are possible 所有的尺寸是获得的

- Emission performance of +/-4dB or better 30MHz-40GHz frequency range。 +/-4dB的辐射性能，或更好的30MHz-40GHz频率范围

- Fully compliant for Immunity in accordance with EN61000.4.3 全兼容用于抗扰度，依照EN61000-4-3.

- Ferrite and Hybrid Lining from 30MHz-40GHz measurements 铁氧体和混合的衬料从30MHz-40GHz测量

- Very cost-effective solution 非常划算的解决

- Flexible modular design enables you to make easy site changes or upgrades灵活的模块设计使得你很容易在现场做改变或升级

Turnkey Systems承包系统:

A complete system approach is available to fully facilitiate your laboratory and includes:

- Electrical distribution 电的分布

- Turntables/Dynomometers 转盘

- Masts 天线塔

- CCTV 有线电视

- Air conditioning 空调

- Fire detection and Surpression 火的监测和超压

- Emission & Immunity Measurement Systems 辐射和抗扰度测量系统

| DB Decibel分贝 DBm Absolute Decibel milliwatt绝对分贝毫瓦 EMC Electromagnetic compatibility电磁兼容 EMPP Electromagnetic Pulse Protection电磁脉冲保护 GHz Gigahertz千兆赫 KHz Kilohertz千赫兹 MHz Megahertz兆赫 MIL – Std Military Standard军用标准 Mm Millimetre毫米 RF Radio Frequency无线电频率 S.E. Shielding Effectiveness屏蔽效能 Sig.Gen. Signal Generator信号发生器 | (More information about shielded doors) |
| --- | --- |

See below a measurement report of an Anechoic Chamber下面是一个电波暗室的测量报告

| Test Frequency 测试频率 | Polarisation 极化 | Field场 |
| --- | --- | --- |
| 10 kHz | Planar平面的 | H |
| 100 kHz | Planar平面的 | H |
| 1 MHz | Planar平面的 | H |
| 100 MHz | Vertical垂直的 | E |
| 500 MHz | Vertical垂直的 | E |
| 1 GHz | Vertical垂直的 | E |
| 5 GHz | Vertical垂直的 | m |
| 10 GHz | Vertical垂直的 | m |
| 18 GHz | Vertical垂直的 | m |

| Frequency | TP1 | TP2 | TP3 | TP4 | TP5 | TP6 |
| --- | --- | --- | --- | --- | --- | --- |
| 10 kHz | -85.16 | -82.15 | -87.88 | -83.08 | -88.08 | -90.08 |
| 100 kHz | -101.22 | -100.16 | -98.16 | -96.09 | -103.25 | -100.70 |
| 1 MHz | -110.59 | -115.02 | -116.24 | -112.45 | -110.02 | -105.51 |
| 100 MHz | -143.67 | -144.59 | -143.15 | -139.89 | -143.18 | -144.54 |
| 500 MHz | -113.36 | -112.35 | -115.00 | -108.85 | -113.62 | -117.07 |
| 1 GHz | -111.77 | -112.21 | -116.34 | -116.38 | -115.68 | -117.19 |
| 5 GHz | -106.97 | -104.41 | -112.78 | -107.80 | -108.15 | -109.67 |
| 10 GHz | -109.75 | -114.50 | -113.53 | -114.82 | -110.56 | -104.24 |
| 18GHz | -109.89 | -104.98 | -108.00 | -110.60 | -107.57 | -115.12 |

| Frequency | TP7 | TP8 | TP9 | TP10 | TP11 | TP12 |
| --- | --- | --- | --- | --- | --- | --- |
| 10 kHz | -90.79 | -87.29 | -81.68 | -87.59 | -88.34 | -85.39 |
| 100 kHz | -106.25 | -99.61 | -102.30 | -95.69 | -105.84 | -96.14 |
| 1 MHz | -110.13 | -111.71 | -106.42 | -106.68 | -108.52 | -107.93 |
| 100 MHz | -143.56 | -146.94 | -142.24 | -143.79 | -141.50 | -139.03 |
| 500 MHz | -111.15 | -110.39 | -111.99 | -109.97 | -117.42 | -109.67 |
| 1 GHz | -109.19 | -111.37 | -111.04 | -115.17 | -112.15 | -108.81 |
| 5 GHz | -101.15 | -103.34 | -104.62 | -107.96 | -104.16 | -109.64 |
| 10 GHz | -109.25 | -109.82 | -104.07 | -113.14 | -111.20 | -111.00 |
| 18GHz | -106.82 | -107.48 | -109.93 | -114.02 | -113.21 | -111.98 |

| Frequency | TP13 | TP14 | TP15 | TP16 | TP17 | TP18 |
| --- | --- | --- | --- | --- | --- | --- |
| 10 kHz | -88.10 | -87.07 | -90.62 | -85.37 | -88.69 | -80.79 |
| 100 kHz | -99.78 | -103.05 | -105.43 | -101.46 | -104.59 | -95.30 |
| 1 MHz | -104.63 | -112.51 | -110.65 | -111.63 | -108.25 | -114.44 |
| 100 MHz | -145.22 | -146.04 | -146.16 | -147.87 | -143.31 | -146.99 |
| 500 MHz | -116.93 | -107.88 | -118.57 | -118.62 | -109.84 | -114.80 |
| 1 GHz | -108.74 | -112.98 | -106.93 | -108.82 | -116.71 | -110.16 |
| 5 GHz | -108.69 | -107.77 | -101.63 | -111.51 | -105.22 | -108.80 |
| 10 GHz | -112.37 | -109.71 | -114.09 | -109.54 | -104.17 | -109.06 |
| 18GHz | -106.48 | -115.29 | -109.67 | -106.81 | -106.28 | -111.99 |