ACQUISITION SYSTEMS FRONTDAQ FD20

- 20 synchronized analog inputs

- Embedded exploitation software

- Web Server

- Upto 7680 samples per second per channel

- Compact Flash

- Ethernet

- Options: GSM, GPS, Monitoring software

Presentation:

Frontdaq is a new design philosophy for AOIP datalogging products.

The user can program, read data, start or stop acquisition from any computer using a simple internet explorer, without needing to install a specific software. All the necessary software are embedded into the datalogger.

Frontdaq is able to store data with a sampling rate up to 7680 samples/second/channel, whatever the number of channels is. All channels are synchronized.

Using a compact flash extension memory, data can be stored for months in addition to its embedded 256MB internal memory.

TTL inputs outputs can be used to automate the acquisition as trigger function.

#### Functions:

20 analog inputs (universal) with scaling (ax+b) and user units

- Voltage: Standard (+/-10V on 11 ranges),

Thermocouples (type K/T/J/N/E/R/S/B)

Strain gauges.(1/4, 1/2, and full bridge)

- Current: 0-20 mA and 4-20 mA with external Shunt

- Resistance: temperature sensors (Pt100, 500, 1000 ohms) 2 or 4 wires,

Resistance (35-2500 Ohms)

4 analog outputs (0-10V), 20 TTL inputs /outputs

Software and resources

* Software in web server mode integrated into the logger for settings, controls, download of stored data. Data can be viewed and downloaded in real time, and simple spreadsheet software can be used to perform exploitation.

* Frontdaq Network Monitor : to check the IP addresses of Frontdaq connected on the network.

* Data are dated and stamped and a large number of exportation files types is available (ASCII, CSV, Excel XML..).

* Internal memory (SDRAM): up to 660.000 samples per channel

* Extension of embedded memory using CF cards

* Communication: TCP/IP (RJ45 10/100), RS232, RS485, Compact flash (extensions GPS...), Wireless (WIFI) .

* Power supply: main or rechargeable battery

Specifications

FRONTDAQ concept

SOFTWARE

STANDARD software) FrontSOFT –Web server access – Access through internet explorer –No nned of DLL or driver

- SetUp, monitoring,

Data import export: ASCII, CSV, Excel, XML... –

Running under Windows, Linux, MacOS.

FrontDAQ Network Monitoring (FNM) – IP adress management

XML Protocole (commands for customer applications (Labview, C++...)).

OPTIONS

VISULOG: Real time monitoring software

Accessories

ACCESSORIES

- External rechargable battery (10h00 - Nimh).

e- PT100 for CJC).

OTHER FRONTDAQ Models

FRONTDAQ 10 ISOLATED CHANNELS       FRONTDAQ: 20 channels extreme temperature confitions

Model FD 10ISO with its battery option      Allow to store data in harsh conditions: from -40°C to +80°C